## Slide 1: Pneumatics
Basic Level

## Slide 2: Pneumatics in Review
Pneumatics has long since played an important role as a technology in the performance of mechanical work. It is used in the development of automated solutions.

## Slide 3: In the majority of applications compressed air is used for one or more of the following functions:
To determine the status of processors (sensors)
Information processing (processors)
Switching of actuators by means of final control elements
Carrying out work (actuators)

## Slide 4: To be able to control machinery and installations necessitates the constructions of a generally complex logic interconnection of statuses are switching conditions. This occurs as a result of the interaction of sensors, processors, control elements and actuators in pneumatic or partly pneumatic systems

## Slide 5: Types of Motion
Linear
Swivel
Rotary

## Slide 6: Some industrial applictions employing pneumatics are listed below:
Clamping
Shifting
Positioning
Orienting
Branching of material flow
Packaging
Filling
Metering
Locking
Driving of axes
Door or chute control

## Slide 7: Advantages of Compressed Air

## Slide 8: Transport
Air can be easily transported in pipelines, even over large distances

## Slide 9: Storage
A compressor need not be in
continuous operation.
Compressed air can be stored in a
reservoir and removed as required.
The reservoir can be transportable.

## Slide 10: Temperature
Compressed air is relatively insensitive
to temperature fluctuations.
This ensures reliable operation, even
under extreme conditions

## Slide 11: Explosion Proof
There is minimal risk of explosion or
fire.
No expensive protection against
explosion is required.

## Slide 12: Cleanliness
Unlubricated exhaust air is clean.
Any unlubricated air does not cause
contamination.
Useful in food, wood and textile
industries.

## Slide 13: Components
Operating components are of simple
construction and therefore relatively
inexpensive.

## Slide 14: Speed
Compressed air is a very fast working
medium.
High working speeds can be obtained.

## Slide 15: Adjustable
With compressed air components,
speeds and forces are infinitely
variable.

## Slide 16: Overload safe
Pneumatic tools and operating
components can be loaded to the point
of stopping and therefore overload
safe.

## Slide 17: Disadvantages of compressed air

## Slide 18: Preparation
Compressed air requires good
preparation.
Dirt and condensate should not be
present.

## Slide 19: Compressible
It is not always possible to achieve
uniform and constant piston speeds
with compressed air.

## Slide 20: Force requirement
Compressed air is economical only up
to a certain force requirement.
At 6-7 bar, and dependent on the travel
and speed, the output limit is between
20000 and 30000 Newtons.

## Slide 21: Noise level
The exhaust air is loud.
The problem is largely solved with new
silencers.

## Slide 22: Costs
Compressed air is a relatively
expensive means of conveying power.
The high energy costs are partially
compensated by inexpensive
components and higher performance.

## Slide 23: Summary of compressed air as a working medium
Advantages:
Air is available everywhere
Compressed air is easily conveyed in pipelines over large distances
Compressed air need not be returned
Compressed air is insensitive to temperature fluctuations
Compressed air is explosion proof
Compressed air is clean
Compressed air is fast

## Slide 24: Summary of compressed air as a working medium 2
Disadvantages:
Straight line movement can be produced directly
Compressed air is a relatively expensive means of conveying energy
Compressed air requires good conditioning
It is only economical up to a certain force expenditure
Air is compressible
Exhaust air is loud (reduced by using silencers)
The oil mist mixed with air for lubricating purposes exhaust or escapes to the atmosphere

## Slide 25: Structure and Signal Flow

## Slide 26: The Structure of Pneumatic Systems

## Slide 27: System circuit diagram

## Slide 28: Components of a Pneumatic System

## Slide 29: Air generation and distribution

## Slide 30: Compressed air production
Energy supply
Compressor
Piston compressors
Flow compressors
After-cooler
Storage
Compressed air receiver
Drying
Absorption drying
Adsorption drying
Low temperature drying
Distribution
Branch line
Ring circuit
Interconnected system
Service unit
Plant

## Slide 31: Types of compressors
Reciprocating piston compressor
Rotary piston compressor
Flow compressor
Piston compressor
Diaphragm compressor
Radial-flow compressor
Axial flow compressor
Sliding vane rotary compressor
Two-axle
Screw
Compressor
Roots blower

## Slide 32: Piston compressor

## Slide 33: Piston compressor 1

## Slide 34: Piston compressor 2

## Slide 35: Piston compressor 3

## Slide 36: Piston compressor 4

## Slide 37: Piston compressor 5

## Slide 38: Piston compressor 6

## Slide 39: Piston compressor 7

## Slide 40: Screw compressor

## Slide 41: Axial compressor

## Slide 42: Axial compressor 1

## Slide 43: Axial compressor 2

## Slide 44: Air receiver
Compressor
Pressure Gauge
Temperature Gauge
Shut Off Valve
Pressure
Relief Valve
Air Receiver
Water Drain

## Slide 45: Air receiver 1
Air receivers are used for
Providing constant air pressure in a pneumatic system regardless of fluctuating consumption
Emergency supply to the system in cases of emergency
The large surface area cools the air
Moisture can be separated from the air

## Slide 46: Air dryers
Water produces
Hardening of seals
Corrosion
Washing out of original lubrication of cylinders
Swelling of seals and diaphragms
Therefore air dryers are used to reduce the moisture content.

## Slide 47: Air dryers 1
Commonly used air dryers are :
Low temperature drying
Adsorption drying
Absorption drying

## Slide 48: Low temperature drying

## Slide 49: Adsorption drying

## Slide 50: Absorption drying

## Slide 51: Air service unit
The air service unit consists of
Air filter
Pressure regulator
Air lubricator
Pressure gauge

## Slide 52: Air service unit 1
The air filter is used for
Preventing dirt particles from entering into the system
Separate condensate out of the compressed air

## Slide 53: Types and sizes of contamination

## Slide 54: Air filter
Inlet
Outlet
Filter Element
Baffles
Water Trap
Drain

## Slide 55: Micro filter

## Slide 56: Pressure regulator
The pressure regulator is used
To provide a constant supply pressure irrespective of the pressure fluctuations in the main line

## Slide 57: Pressure regulator 1

## Slide 58: Pressure Regulator 2
Valve Body
Inlet
Outlet
Vent
Adjusting screw
Pressure operation
Spring

## Slide 59: Pressure regulator 3
6 Bar

## Slide 60: Pressure regulator 4
6 Bar

## Slide 61: Pressure regulator 5
6 Bar

## Slide 62: Pressure regulator 6
6 Bar

## Slide 63: Pressure regulator 8
6 Bar

## Slide 64: Pressure regulator 9
6 Bar

## Slide 65: Pressure regulator 10
6 Bar

## Slide 66: Pressure regulator 11
6 Bar

## Slide 67: Pressure regulator 12
6 Bar

## Slide 68: Pressure regulator 13
6 Bar
4 Bar

## Slide 69: Pressure regulator 14
6 Bar
4 Bar

## Slide 70: Pressure regulator 15
6 Bar
4.5 Bar

## Slide 71: Pressure regulator 16
6 Bar
4.5 Bar

## Slide 72: Pressure regulator 17
6 Bar

## Slide 73: Air lubricator
The air lubricator is used
Extremely rapid oscillating motions are required
With cylinders with large diameters ( 125mm diameter)

## Slide 74: Air lubricator 1
Drip chamber
Viaduct
Duct
Check valve
Ball seat
Riser
Oil
Pressure
regulator
Lubricator
Filter unit

## Slide 75: Air lubricator 2

## Slide 76: Air lubricator 3

## Slide 77: Air service unit 2

## Slide 78: Air service unit 3

## Slide 79: Air service unit symbol

## Slide 80: Air service unit 4

## Slide 81: Air service unit 5

## Slide 82: Air service unit 6

## Slide 83: Piping system (air distribution)
Diameter of pipe-lines depends on:
Flow volume
  I.e. Volume diameter
Pipe length
  I.e. Longer length diameter
  Otherwise, pressure drop is high
Pressure drop
  Permissible pressure drop between receiver and user should not be more than 0.1 bar

## Slide 84: Piping system (air distribution) 1
Working pressure
  Should not be more than 0.1 bar.
Number of restrictions
  I.e. Number of resistance to flow; Example: shut-off valves, bends, t-joints, etc.

## Slide 85: Air distribution
1-2% Gradient

## Slide 86: Air distribution (air ring main)
Production Plant

## Slide 87: Air distribution (ring main cross-connected)
Production Plant

## Slide 88: Valves
The function of valves is to control the pressure or flow rate of pressure media.

## Slide 89: The Valve is Described by:
Number of ports or openings (ways):
Number of positions:
Methods of actuation of the valve:
Methods of return actuation:
2-way, 3-way, 4-way, 5-way, etc.
2 pos., 3 pos.
Manually, mechanically, pneumatically, electrically
Spring return, air return

## Slide 90: 3/2-way valve
3/2-way valve, normally closed, disc seat
3 working ports, 2 switching positions
Unactuated A spring-loaded disc blocks flow from supply port 1 to working port 2. Working port 2 is connected to exhaust port 3.
Actuated Exhaust port 3 is closed first and then flow is opened from port 1 to port 2.
Characteristics
Non-overlapping switching
Large flow cross section with short actuation stroke
Insensitive to dirt
Long service life

## Slide 91: 5/2-way double pilot valve
5/2-way double pilot valve, longitudinal slide 5 working ports, 2 switching positions
The valve has a memory function, a short signal (pulse) is sufficient for reversing.
A pneumatic signal at pilot port 12 causes flow from port 1 to port 2.
A pneumatic signal at pilot port 14 causes flow from port 1 to port 4.
If signals are applied at both pilot ports, the first incoming signal is dominant.
Characteristics
For the actuation of double-acting cylinders
Long actuation strokes
Small actuating forces

## Slide 92: Non-return Valves
The non-return valve allows a signal to flow through the device in one direction and in the other direction blocks the flow.

## Slide 93: Shuttle valve
The shuttle valve is used for logic OR operation.
Pneumatic signals at input 1, input 1(3) or at both inputs result in a signal at output 2.
No input signal results in no output signal.
Output signals
If signals are applied at both inputs, the signal with the higher pressure reaches the output.

## Slide 94: Dual pressure valve
The dual pressure valve is used for logic AND operations.
Pneumatic signals at inputs 1 and 1(3) results in a signal at output 2.
No input signal or only one input signal results in no output signal.
Output signals
In the case of time differences in the input signals, the last incoming signals reaches the output.
In the case of pressure differences with input signals, the signal with the lower pressure reaches the output.

## Slide 95: Non-return valve and quick exhaust valve
Non-return valve
Releases flow in one direction
Shuts of flow in the opposite direction
The seal lifts off its seat if the force of compressed air is greater than the pretension force of the spring.
Quick exhaust valve
Used for quick exhausting of working components
The piston speed of a cylinder can be increased to virtually the maximum possible value, since the flow resistance of the exhaust air is reduced during the motion.
Installed directly on or as near as possible to the cylinder

## Slide 96: Flow Control Valves
The flow control valve restricts of throttles the air in a particular direction to reduce the flow rate of the air and hence control the signal flow.

## Slide 97: Flow control valve and one-way flow control valve
Flow control valve
Flow control valves influence the volumetric flow rate of compressed air.
Flow control valves are generally adjustable; the setting can be locked.
Never close flow control valves completely.
One-way flow control valve
Valve combination of flow control valve and non-return valve
Facilitates free flow in one direction; in the opposite direction compressed air can only flow through the set cross section
Installed directly on the cylinder or as near as possible

## Slide 98: Single acting cylinder
Operation

## Slide 99: Single acting cylinder 1
Operation

## Slide 100: Single acting cylinder 2
Operation
Force = Pressure x Area (piston)

## Slide 101: Single acting cylinder 3
Operation
Force = Pressure x Area (piston)

## Slide 102: Single acting cylinder 4
Operation
Force = Pressure x Area (piston)

## Slide 103: Single acting cylinder 5
Operation
Force = Pressure x Area (piston)

## Slide 104: Single acting cylinder 6
Operation
Force = Pressure x Area (piston)

## Slide 105: Single acting cylinder 7
Operation
Force = Pressure x Area (piston)

## Slide 106: Single acting cylinder 8
Operation

## Slide 107: Single acting cylinder 9
Operation

## Slide 108: Single acting cylinder 10
Operation

## Slide 109: 11
Operation

## Slide 110: Single acting cylinder 12
Operation

## Slide 111: Single acting cylinder 13
Operation

## Slide 112: Single acting cylinder 14
Operation

## Slide 113: Double acting cylinder
With end position cushioning
Designed to protect the piston and end caps of the cylinder from impact damage.

## Slide 114: Double acting cylinder 1
With end position cushioning
adjustable

## Slide 115: Double acting cylinder 2
Cushioning sleeves
Cushioning adjustment
Seals
Non-return valve

## Slide 116: Double acting cylinder 3

## Slide 117: Double acting cylinder 4

## Slide 118: Double acting cylinder 5

## Slide 119: Double acting cylinder 6

## Slide 120: Double acting cylinder 7

## Slide 121: Double acting cylinder 8

## Slide 122: Double acting cylinder 9

## Slide 123: Double acting cylinder 10

## Slide 124: Double acting cylinder 11

## Slide 125: Double acting cylinder 12

## Slide 126: Double acting cylinder 13

## Slide 127: Double acting cylinder 14

## Slide 128: Double acting cylinder 15

## Slide 129: Double acting cylinder 16

## Slide 130: Double acting cylinder 17

## Slide 131: Double acting cylinder 18

## Slide 132: Double acting cylinder 19

## Slide 133: Double acting cylinder 20
With end position cushioning
Protects cylinder end caps and piston from impact damage.
Allows delicate components to be moved quickly but located gently.
Reduces vibration and shock loads.

## Slide 134: Systems
Generally, the actuation of a cylinder is effected via a directional control valve. The choice of such a directional control valve is dependent on the respective application.

## Slide 135: Control Circuit for the Single-Acting Cylinder
The purpose of pneumatic drives is to convert the energy stored in the compressed air into kinetic energy.
Mode of operation
With single-acting cylinders, the piston is pressurised at one end only. The cylinder can only carry out work in this direction (working stroke).
The return stroke of the piston rod is effected via a built-in spring, i.e. an external force (idle stroke).
Actuation
3/2-way valve

## Slide 136: A 3/2 way valve controls the single-acting cylinder.

## Slide 137: Control circuit for the double-acting cylinder
Double-acting cylinder
Mode of operation
With double-acting cylinders, the piston is pressurised at both ends. The cylinder can operate in both directions.
Piston force In the case of cylinders with piston rod at one end, the force of the advance stroke is greater than that of the return stroke (piston surface/annular surface ratio).
End position cushioning Used for large moving loads to prevent hard piston impact. A cushioning piston interrupts the direct exhaust path. The air has to flow through a small, generally adjustable cross section.
Actuation 5/2-way valve, 5/3-way valve

## Slide 138: A 5/2-way directional control valve control the double acting cylinder.

## Slide 139: Symbols and Standards in Pneumatics

## Slide 140: The development of pneumatic systems is assisted by a uniform approach to the representation of the elements and the circuits. The symbols used for the individual elements must display the following characteristics:
  Function
  Actuation and return actuation methods
  Number of connections
  Number of switching positions
  General operating principle
  Simplified representation of the flow path

## Slide 141: Pneumatic symbols
A symbol does not represent the
following characteristics:
  Size or dimensions of the component
  Particular manufacturer, methods of construction or costs
  Operation of the ports
  Any physical details of the elements
  Any unions or connections other than junctions
The standard used is ISO 1219

## Slide 142: Energy supply
Compressor with fixed capacity
Air receiver and ‘T’ junction

## Slide 143: Air service equipment
Air filter
Air lubricator
Pressure regulator

## Slide 144: Air service equipment 1
Air service unit
Filter
Regulator
Gauge
Lubricator
Simplified air
Service unit

## Slide 145: Directional control valves

## Slide 146: Directional control valves 1

## Slide 147: Numbering Systems

## Slide 148: Directional control valves 2

## Slide 149: Methods of Actuation
Manually Actuated
Mechanically Actuated
Pneumatically Actuated
Electrical and
Combined Actuation

## Slide 150: Directional control valves 3
Methods of actuation
Mechanical
General manual operation
Push button
Lever operated
Detent lever operated

## Slide 151: Directional control valves 4
Methods of actuation
Mechanical
Foot pedal
Roller operated
Idle return, roller

## Slide 152: Directional control valves 5
Methods of actuation
Mechanical
Spring return
Spring centered

## Slide 153: Directional control valves 6
Methods of actuation
Pneumatic
Direct pneumatic actuation
Indirect pneumatic
actuation (piloted)

## Slide 154: Non-return valves 1
Check valve
Spring loaded check valve
Shuttle valve: ‘or’ function

## Slide 155: Non-return valves 2
Two pressure valve:
‘AND’ function
Quick exhaust valve

## Slide 156: Flow control valves 3
Flow control valve adjustable
One-way flow control valve

## Slide 157: Pressure valves
Adjustable pressure regulating valve,
non-relieving type
Adjustable pressure regulating valve,
relieving type (overloads are vented)

## Slide 158: Pressure valves 1
Sequence valve combination

## Slide 159: Linear actuators
Single acting cylinder
Double acting cylinder
Double acting cylinder with
double ended piston rod
Rodless cylinder

## Slide 160: Linear actuators 1
Double-acting cylinder with non-adjustable
cushioning in one direction
Double-acting cylinder with single adjustable
cushioning
Double-acting cylinder with adjustable
cushioning at both ends

## Slide 161: Rotary actuators
Air motor, rotation in one direction, fixed capacity
Air motor, rotation in one direction, variable capacity
Air motor, rotation in both directions, variable capacity
Rotary actuator, limited travel, rotation in both directions

## Slide 162: Auxiliary symbols
Exhaust port
Exhaust port with threaded connection
Silencer
Line connection

## Slide 163: Auxiliary symbols 1
Crossing lines (not connected)
Pressure gauge
Visual indicator

## Slide 164: Methods for the Development of Pneumatic Systems

## Slide 165: Control Chain

## Slide 166: Design of The Circuit Diagram

## Slide 167: Circuit diagram

## Slide 168: Designation of Individual Elements
Normal Position
The normal position on valves with existing reset, eg. spring, refers to the switching position assumed by the moving parts of the valve, if the valve is not connected.

## Slide 169: Designation of Individual Elements 1
Initial Position
The initial position is the switching position assumed by the moving parts of a valve after the valve has been installed in a system and the system pressure has been switched on and possibly also the electrical voltage, and with which the designated switching program starts.

## Slide 170: Designation of Individual Elements
Signal elements should be represented in the normal position in the circuit diagram. If valves are actuated in the initial position as a start precondition, this must be indicated by the representation of a trip cam.
Actuated Initial Position

## Slide 171: Designation by Numbers
What this type of designation, elements are divided into groups. Group 0 contains the elements for the power supply, groups 1,2 designate the individual control chains. One group number is generally allocated for each cylinder.

## Slide 172: Designation by Letters
This type of designation is used primarily for a systematic development of circuit diagrams. Here, limit switches are allocated to the cylinder, which acknowledges them

## Slide 173: Summary
Physical arrangement of the elements is ignored.
Draw the cylinders and directional control valves horizontally wherever possible.
The energy flow within the circuit moves from the bottom to the top.
Energy source can be shown in simplified form.
Show elements in the initial position of the control. Identify actuated elements by a cam.
Draw pipelines straight without cross-over wherever possible.

## Slide 174: Development of Single Actuator Circuits

## Slide 175: Direct Control of a Pneumatic Cylinder
The simplest level of control for the single or double-acting cylinder involves direct control signals. With this, the cylinder is actuated directly via a manually of mechanically actuated valve, without any intermediate switching of additional directional control valves. If the port sizes and the flow values of the valve are too large, the operating forces required may be too great for direct manual operation.

## Slide 176: Direct Control of a Single-acting Cylinder
A single-acting cylinder of 25mm diameter is to clamp a component when a push button is pressed. As long as the push button is activated, the cylinder is to remain in the clamped position. If the push button is released, the clamp is to retract.

## Slide 177: Solution
The control valve used for the single-acting cylinder is the 3/2-way valve. In this case, since the cylinder is of small capacity, is of small capacity, the operation can be directly controlled by a push button 3/2-way directional control valve with spring return.
Circuit Diagram

## Slide 178: Direct Control of a Double-acting Cylinder Exercise
The Problem
A double-acting cylinder is to extend when a push button is operated. Upon release of the push button the cylinder is to retract. The cylinder is of small bore (25 mm diameter) requiring a small flow rate to operate at the correct speed.
Draw the circuit diagram for the problem.
Designate the valves and indicate the numbering system for the connections (ports).

## Slide 179: Direct Control of a Double-acting Cylinder
Questions
What happens to the cylinder, if the push button is pressed for a very short period, and is then immediately released?
Describe the operation of the circuit?

## Slide 180: Direct Control of a Double-acting Cylinder 1
Solution

## Slide 181: Exercise 1 Pressing of Cheese Wheels
Cheese wheels are to be manually inserted into the device.
Actuation of the pushbutton is to cause the cylinder to advance and press the cover onto the device.
The pushbutton is to be pressed until the pressing operation is completed.
If the pushbutton is released, the cylinder is to retract again and release the device.
The wheel can then be removed.

## Slide 182: Single-acting cylinder
The purpose of pneumatic drives is to convert the energy stored in the compressed air into kinetic energy.
Mode of operation
With single-acting cylinders, the piston is pressurised at one end only. The cylinder can only carry out work in this direction (working stroke).
The return stroke of the piston rod is effected via a built-in spring, i.e. an external force (idle stroke).
Actuation
3/2-way valve

## Slide 183: Piston force
The piston force exerted by the cylinder is dependent upon the air pressure, the cylinder diameter and the frictional resistance of the sealing components. The theoretical piston force is calculated by the formula:
Fth = A • p
Fth = Theoretical piston Force (N)
A = Useful piston Area (m2)
p = Operating Pressure (Pa)

## Slide 184: Derived Units

## Slide 185: Design and Mode of Operation of a Single-Acting Cylinder
Fth = A * P
A = D² * π 4
D = Info is in the data sheets for the single acting cylinder.
Feff = A * p – (FF + FR)
FF = 10% of the Fth
FR = Info is in the data sheets for the single acting cylinder.

## Slide 186: Design and Mode of Operation of a Single-Acting Cylinder Solution
Fth = A * P
Fth = .000314159 * 600000
Fth = 188.4956
A = D² * π 4
A = .02² * π 4
A = .000314159
P = 600000
Feff = A * p – (FF + FR)
Feff = .000314159 * 600000 – (18.85 + 13.6)
Feff = 156.0454
FF = 188.4956 * .10
FF = 18.85
FR = 13.6

## Slide 187: 3/2-way valve 1
3/2-way valve, normally closed, disc seat
3 working ports, 2 switching positions
Unactuated A spring-loaded disc blocks flow from supply port 1 to working port 2. Working port 2 is connected to exhaust port 3.
Actuated Exhaust port 3 is closed first and then flow is opened from port 1 to port 2.
Characteristics
Non-overlapping switching
Large flow cross section with short actuation stroke
Insensitive to dirt
Long service life

## Slide 188: Exercise 1
Solution

## Slide 189: Exercise 2 Openings of an Animal Feed Silo
Operation of the pushbutton actuator is to cause the cylinder to retract until the retracted end position is reached.
The pushbutton actuator is to be operated for as long as the slide is to remain open.
If the pushbutton actuator is released again, the cylinder is to advance thus causing the slide to close the silo opening.

## Slide 190: Exercise 2
Solution

## Slide 191: Exercise 3 Testing of Key Blanks
Key blanks are to be inserted manually into the test device.
Actuation of the selector switch is to cause the cylinder to advance and secure the key blanks.
The cylinder is to remain in this position even after the selector switch is released.
Resetting of the selector switch is to cause the cylinder to return into the retracted end position and to remain there until the selector switch is actuated again.

## Slide 192: Exercise 3
Solution

## Slide 193: Exercise 4 Sorting of Packages
Actuation of the selector switch is to cause the cylinder to advance and push the slide into the material flow.
The cylinder is to remain in the position even after the selector switch is released and the material flow is to remain interrupted.
Resetting of the selector switch is to cause the cylinder to return into the retracted end position and release the material flow again.
The cylinder is to remain in this position until the selector switch is actuated again.

## Slide 194: Double-acting cylinder
Cylinder design and sealing types
Design
Cylinder barrel
End and bearing caps
Piston with seal
Piston rod
Bearing bush
Scraper ring
Connection ports
Seals
Reset spring (single-acting cylinders only)
Sealing types
Function: The mutual sealing of chambers
Installation criteria: Dimensions, fitting accuracy, frictional force, service life, chemical resistance
Materials: BUNA-N, viton, PTFE

## Slide 195: Double-acting cylinder 1

## Slide 196: Design and Mode of Operation of a Double-Acting Cylinder
Advance Stroke
Feff = (A * p) – FF
A = D² * π 4
FF = approx. 10% of Fth
Fth = A * P
Return Stroke
Feff = (A’ * p) – FF
A’ =(D² - d²) * π 4
FF = approx. 10% of Fth
Fth = A’ * P

## Slide 197: Design and Mode of Operation of a Double-Acting Cylinder Advanced Stroke Solution
Fth = A * P
Fth = .000314159 * 600000
Fth = 188.4956
A = D² * π 4
A = .02² * π 4
A = .000314159
P = 600000
Feff = A * p – FF
Feff = .000314159 * 600000 – 18.85
Feff = 169.65
FF = 188.4956 * .10
FF = 18.85

## Slide 198: Design and Mode of Operation of a Double-Acting Cylinder Return Stroke Solution
Fth = A’ * P
Fth = .000314159 * 600000
Fth = 158.34
A = (D² - d²) * π 4
A = (.02² - .008²) * π 4
A = .000263894
P = 600000
Feff = A’ * p – FF
Feff = .000263894 * 600000 – 15.834
Feff = 142.5
FF = 158.34 * .10
FF = 15.834

## Slide 199: 5/2-way double pilot valve 1
5/2-way double pilot valve, longitudinal slide 5 working ports, 2 switching positions
The valve has a memory function, a short signal (pulse) is sufficient for reversing.
A pneumatic signal at pilot port 12 causes flow from port 1 to port 2.
A pneumatic signal at pilot port 14 causes flow from port 1 to port 4.
If signals are applied at both pilot ports, the first incoming signal is dominant.
Characteristics
For the actuation of double-acting cylinders
Long actuation strokes
Small actuating forces

## Slide 200: Exercise 4
Solution

## Slide 201: Indirect Control of a Pneumatic Cylinder
Cylinders with a large piston diameter have a high air requirement. A control element with high nominal flow rate must be used to actuate these. If the force should prove too high for a manual actuation of the valve, then an indirect actuation should be constructed, whereby a signal is generated via a second smaller valve which will provide the force necessary to switch the control element.

## Slide 202: Indirect Control of a Single-Acting Cylinder
A single-acting cylinder with a large piston diameter is to clamp a work piece following actuation of a pushbutton. The cylinder is to retract once the pushbutton is released.

## Slide 203: Indirect Control of a Single-Acting Cylinder 1
Solution
In the initial position, the single-acting cylinder 1A is retracted. A spring return 3/2-way pneumatic valve is used to actuate the cylinder. Connection 1 of the valve 1V is closed, connection 2 is exhausted to atmosphere via connection 3.

## Slide 204: Indirect Control of a Double-Acting Cylinder Exercise
A double-acting cylinder is to advance when a push button is operated. Upon release of the push button the cylinder is to retract. The cylinder is 250 mm diameter and consumes a large volume of air.

## Slide 205: Indirect Control of a Double-Acting Cylinder
Questions
What happens to the cylinder, if the push button is pressed for a very short period and is then immediately released?
Describe the operation of the circuit.

## Slide 206: Indirect Control of a Double-Acting Cylinder 2
Solution

## Slide 207: Exercise 5 Stopping Crates of Drinks
Actuation of a selector switch is to cause the cylinder to advance and push the slide into the material flow; the crates are thus stopped.
Resetting of the selector switch is to cause the cylinder to return into the retracted end position and once again release the flow of material.
It is to remain in this position until the selector switch is actuated again.

## Slide 208: Exercise 5
Solution

## Slide 209: Logic Functions: AND, OR
The pneumatic shuttle valve and the dual pressure valve have logic functions. Both have two inputs and one output each. The shuttle valve has the characteristics of an OR function, whereby at least either of two inputs 1 or 1(3) are required to generate an output at port 2 of the valve. In the case of the dual pressure valve, the characteristic is that of the AND function, whereby both inputs 1 and 1(3) are required to initiate an output 2.

## Slide 210: The Logic AND Function
The piston rod of a double-acting cylinder is to advance when the 3/2-way roller lever valve 1S2 is actuated and the pushbutton of the 3/2-way valve 1S1 is actuated. If either of these are released, then the cylinder is to return to the initial position.

## Slide 211: The Logic AND Function 1
Dual Pressure Valve Solution
Series Solution

## Slide 212: The Logic AND Function Exercise
The piston rod of the cylinder 1A is to advance only if a work piece is inserted in the work piece retainer, a guard has been lowered and the operator presses the push button valve. Upon release of the pushbutton or if the guard is no longer in its lower position, the cylinder 1A is to retract to the initial position.

## Slide 213: The Logic AND Function 2
Questions
What happens to the cylinder, if the pushbutton is pressed for a very short period and is then immediately released?
Describe the operation of the circuit.

## Slide 214: The Logic AND Function 3
Solution

## Slide 215: The Logic OR Function
A double acting cylinder is to advance if one of two push buttons is operated. If the push button is then released, the cylinder is to retract.

## Slide 216: The Logic OR Function
Solution

## Slide 217: The Logic OR Function Exercise
A double-acting cylinder is used to transfer parts from a magazine. If either a pushbutton or a foot pedal is operated, the cylinder is to advance. Once the cylinder is fully advanced, it is to retract tot the initial position. A 3/2-way roller lever valve it to be used to detect the full extension of the cylinder.

## Slide 218: The Logic OR Function 1
Questions
What happens to the cylinder, if the push button or pedal are pressed for a very short period and then immediately released?
Describe the operation of the circuit?

## Slide 219: The Logic OR Function 2
Solution

## Slide 220: Memory Circuit and Speed Control of a Cylinder.
The piston rod of a double-acting cylinder is to advance when a 3/2-way push button valve is actuated manually. The cylinder is to remain advanced until a second valve is actuated. The signal of the second valve can only take effect after the first valve has been released. The cylinder is to remain in the initial position until a new start signal is given. The speed of the cylinder is to be adjustable in both directions.

## Slide 221: Flow control valve and one-way flow control valve 1
Flow control valve
Flow control valves influence the volumetric flow rate of compressed air.
Flow control valves are generally adjustable; the setting can be locked.
Never close flow control valves completely.
One-way flow control valve
Valve combination of flow control valve and non-return valve
Facilitates free flow in one direction; in the opposite direction compressed air can only flow through the set cross section
Installed directly on the cylinder or as near as possible

## Slide 222: Supply Air Throttling and Exhaust Air Throttling
Supply Air Throttling
One-way flow control valves are installed so that the air entering the cylinder is throttled. The exhaust air can escape freely through the check valve of the throttle valve on the outlet side of the cylinder.
Exhaust Air Throttling
The supply air flows freely to the cylinder and the exhaust air is throttled. In this case, the piston is loaded between two cushions of air. The first cushion effect is the supply pressure to the cylinder and the second cushion is the exhausting air being restricted at the one-way flow control valve orifice. Arranging throttle relief valves in this way contributes substantially to the improvement of feed behavior.

## Slide 223: Memory Circuit and Speed Control of a Cylinder. 1
4/2-way or 5/2-way double pilot valves possess the required memory function. The valve retains its last switched position until an opposing signal is received. The characteristic is independent of the time period, for which the signal is applied to the switching valve.
The one way flow control valves control the cylinder speed in both directions and are independently adjustable. Since the displaced air flow is restricted in each case, this is an exhaust air flow control.

## Slide 224: Memory Circuit and Speed Control of a Cylinder. 2
Solution

## Slide 225: Memory Circuit and Speed Control of a Cylinder Exercise.
A double-acting cylinder is to be used to transfer parts from a magazine. The cylinder is to advance fully when a push button is operated and then retract automatically. Full extension is confirmed by a roller lever valve. The cylinder is to continue forward even if the push button is released before full extension is reached. The speed of the cylinder is to be adjustable in both directions.

## Slide 226: Memory Circuit and Speed Control of a Cylinder
Questions
What is the effect on the piston rod movement, if the push button remains actuated once the piston rod has reached the end position?
What is the effect on the advance stroke, if the roller lever valve is fitted at the stroke mid position of the piston rod?
Describe the initial status of the system.
Describe the operation of the circuit.

## Slide 227: Memory Circuit and Speed Control of a Cylinder 1
Solution

## Slide 228: Exercise 6 Opening and Closing of a Pipe
The slide in a pipe is to be opened and closed. Actuation is to be triggered by means of a valve with selector switch. A double-acting cylinder is to be used as the drive.
The slide is to open/close only gradually since the load on the pipe would otherwise be to great.

## Slide 229: Exercise 6
Solution

## Slide 230: Exercise 7 Shutting Off Using a Quick Shut-off Function
A filling plant fills pots of paint with wall and ceiling paint. The pipes through which the paint flows are to close quickly. The opening of the pipe is to be effected gradually.
Actuation of a selector switch is to cause a shut-off valve to open gradually.
Resetting of the selector switch is to cause the shut-off valve to close quickly.

## Slide 231: Exercise 7
Solution

## Slide 232: The Quick Exhaust Valve Exercise
The combined actuation of a manually actuated valve and a roller lever valve advances a forming tool on an edge-folding device. The forming tool is driven by a double-acting cylinder. For rapid forward travel, the circuit utilizes a quick exhaust valve. The retracting speed is to be adjustable. If either of the two valves are released, the tool returns to its initial position.

## Slide 233: The Quick Exhaust Valve
Question
What happens to the cylinder if the push button is pressed for a short period and then released?
Describe the operation of the circuit.

## Slide 234: The Quick Exhaust Valve 1
Solution
The combined actuation of a manually actuated valve and a roller lever valve advances a forming tool on an edge-folding device. The forming tool is driven by a double-acting cylinder. For rapid forward travel, the tool is driven by a double-acting cylinder. For rapid forward travel, the circuit utilizes a quick exhaust valve. The retracting speed is to be adjustable. If either of the two valves are released, the tool returns to its initial position.

## Slide 235: Exercise 8 Actuation of a Shut-off Device
The slide of a plastic granulate filling system is to close quickly. The opening of the slide is to be effected gradually.
Actuation of a pushbutton is to cause a shut-off device (ball valve) to open gradually.
Actuation of a second pushbutton is to cause the shut-off device to close quickly.

## Slide 236: Exercise 8
Solution

## Slide 237: Exercise 9 Brushing of Cheese Wheels
Cheese wheels are to be brushed during production. Loading of the brushing device is to be controlled manually. The cheese wheels are to be supplied via a conveyor. Material flow is to be stopped by means of a slide if the device is filled.
Actuation of the pushbutton is to cause the cylinder to advance and push the slide into the material flow.
The cylinder retains this position even after the pushbutton is released and material flow is to remain interrupted.
Actuation of the second pushbutton is to cause the cylinder to return into the retracted end position and release material flow again.
It is to remain there until the first pushbutton is actuated again.

## Slide 238: Exercise 9
Solution

## Slide 239: Exercise 10 Clamping of a Workpiece
An automatic rotary indexing machines is used in production for the feeding of workpieces. Workpieces to be processed are to be clamped in the individual workpiece retainers. A clamping device is to be designed and checked by means of a test setup.
A double-acting cylinder is to advance only if a pushbutton is actuated AND if the cylinder is in the retracted end position at the same time, since it is otherwise not possible to insert a workpiece for processing.
The clamping cylinder is to retain the forward end position until the workpiece is processed. The duration of the processing time can vary.
Pressing of a second pushbutton is to cause the workpiece to be released.

## Slide 240: Exercise 10
Solution

## Slide 241: Exercise 11 Actuation of a Sliding Door
A Sliding door is to be opened and closed from both sides by means of a pushbutton. Only one pushbutton is to be located on each of the door in order to eliminate incorrect operation in cases of emergency.
Provided that the sliding door is in a defined end position, it can be moved into the opposite end position by means of pressing a button. The sliding door can thus be opened or closed.
It is not possible to start the opening or closing function for as long as the door is not in an end position.

## Slide 242: Exercise 11
Solution

## Slide 243: Exercise 12 Feeding of Workpieces
Workpieces are to be fed from a magazine towards a machining process. The ejecting of a workpiece must be prevented it the removal position is not clear.
The ejecting function is to be started by means of a pushbutton if the cylinder is in the retracted end position. The ejecting cylinder is to push a workpiece form the magazine only if a sensor in the removal area signals that the removal position is NOT occupied.
If the removal position is clear, the cylinder is to move into the forward end position with exhaust air restricted, eject the workpiece and immediately return into the retracted end position.

## Slide 244: Exercise 12
Solution

## Slide 245: Exercise 13
Solution

## Slide 246: Exercise 14
Solution

## Slide 247: Exercise 15
Solution

## Slide 248: Exercise 16
Solution

## Slide 249: Exercise 17
Solution

## Slide 250: Exercise 18
Solution