## Slide 1: Electropneumatic
Basic Level

## Slide 2: Control Systems
Both pneumatic and electropneumatic controllers have a pneumatic power section. The signal control section varies according to type.

## Slide 3: Pneumatic Control
In a pneumatic control pneumatic components are used, that is , various types of valves, sequences, air barriers, etc.

## Slide 4: Electro-Pneumatic Control
In and electro-pneumatic control the signal control section is made up of an electrical components, for example with electrical input buttons, proximity switches, relays, or a programmable logic controller.

## Slide 5: 1
The directional control valve form the interface between the signal control section and the pneumatic power section in both types of controller.

## Slide 6: 2
In contrast to a purely pneumatic control system, electropneumatic controllers are not known in any single overall circuit diagram, but in two separate circuit diagrams.

## Slide 7: Electropneumatic Components
Switches,
Coils
Relays
Sensors
Directional Control Valves

## Slide 8: Normally open switch

## Slide 9: Normally closed switch

## Slide 10: Changeover switch

## Slide 11: Switches

## Slide 12: Momentary and sustained switches

## Slide 13: Switches 1

## Slide 14: Sustained normally open switch

## Slide 15: Changeover switch 1

## Slide 16: Normally open contact

## Slide 17: Normally closed contact

## Slide 18: Changeover contact

## Slide 19: Contacts

## Slide 20: Switches 2

## Slide 21: Typical push button switches

## Slide 22: Mechanical limit switch
1: Reset spring
2: Housing
3: Swing lever
4: Guide pin
5: Leaf spring
6: Contact spring
Normally open contact
Normally close contact

## Slide 23: Mechanical limit switch 1

## Slide 24: Relays

## Slide 25: Relays 1
A Relay has Certain Characteristics
Low Maintenance
Able to Switch a Number of Independent Circuit Paths
Easily Adaptable to Various Operating Voltages
High Operating Speed, ie. Short Switching Times
Can be Used as a Logic or Interlocking Device

## Slide 26: Relay Contact Configuration

## Slide 27: Reed Switches

## Slide 28: Reed Switches 1

## Slide 29: Pressure Switches

## Slide 30: Inductive Sensors

## Slide 31: Inductive Sensors 1

## Slide 32: Inductive Sensors 2

## Slide 33: Capacitive Sensors

## Slide 34: Through Beam Sensors

## Slide 35: Retro-Reflective Sensors

## Slide 36: Diffuse Sensors

## Slide 37: Directional control valves

## Slide 38: Design principles
The design of control valves are categorized as
Poppet valves
  Ball seat valves
  Disc seat valves
Slide valves
  Longitudinal slide valve
  Longitudinal flat slide valve

## Slide 39: Poppet valves

## Slide 40: Slide valves

## Slide 41: Symbol development

## Slide 42: Ports and Positions

## Slide 43: Solenoid valves
The directional control valves used in electropneumatics are similar to those used in pure pneumatics. The only difference is that they are actuated by solenoids.

## Slide 44: Solenoids

## Slide 45: 2/2-way single solenoid valve

## Slide 46: 3/2-way single solenoid valve

## Slide 47: 3/2-way single solenoid valve 1

## Slide 48: Pilot signal flow
ELECTRICAL SIGNAL
APPLIED TO
SOLENOID
SOLENOID ACTUATES
PILOT VALVE
PILOT ACTUATES
MAIN VALVE

## Slide 49: Pilot control

## Slide 50: 3/2-way single solenoid valve with pilot control

## Slide 51: 3/2-way single solenoid valve with pilot control 1

## Slide 52: 3/2-way single solenoid valve with pilot control 2

## Slide 53: 5/2-way single solenoid valve with pilot control

## Slide 54: 5/2-way single solenoid valve with pilot control 1
2 (B)
3 (R)
1 (P)
5 (A)
4 (S)

## Slide 55: 5/2-way single solenoid valve with pilot control 2
5 (A)
4 (S)
1 (P)
2 (B)
3 (R)

## Slide 56: 5/2-way single solenoid valve with pilot control 3
5 (A)
4 (S)
1 (P)
2 (B)
3 (R)

## Slide 57: 5/2-way single solenoid valve with pilot control 4
2 (B)
3 (R)
1 (P)
5 (A)
4 (S)

## Slide 58: 5/2-way single solenoid valve with pilot control 5
5 (A)
4 (S)
1 (P)
2 (B)
3 (R)

## Slide 59: 5/2-way single solenoid valve with pilot control 6
5 (A)
4 (S)
1 (P)
2 (B)
3 (R)

## Slide 60: 5/2-way single solenoid valve with pilot control 7
5 (A)
4 (S)
1 (P)
2 (B)
3 (R)

## Slide 61: 5/2-way single solenoid valve with pilot control 8
5 (A)
4 (S)
1 (P)
2 (B)
3 (R)

## Slide 62: 5/2-way single solenoid valve with pilot control 9
2 (B)
3 (R)
1 (P)
5 (A)
4 (S)

## Slide 63: 5/2-way double solenoid valve with pilot control

## Slide 64: 5/3-way double solenoid valve with pilot control

## Slide 65: 5/3-way double solenoid valve with pilot control 1

## Slide 66: 5/3-way double solenoid valve with pilot control 2

## Slide 67: 5/3-way double solenoid valve with pilot control 3
5
3
4
2
5
4
1
3
2
5
4
1
3
2

## Slide 68: Pneumatic Cylinders
Single Acting
Double Acting

## Slide 69: Single acting cylinder
Construction

## Slide 70: Single acting cylinder 1
Construction
Piston
Rod
Spring
Connection
Seal
Bearing
Vent

## Slide 71: Single acting cylinder 2
Diameters 10mm to 32mm
Stroke Lengths 5mm to 50mm

## Slide 72: Double acting cylinder
With magnetic piston
Designed to allow the position of the piston to be monitored by appropriate devices.

## Slide 73: Double acting cylinder 1
With adjustable end position cushioning
and magnet in piston

## Slide 74: Double acting cylinder 2
Magnets incorporated in/around piston
Magnetic field extends outside body of cylinder
Sensors can be positioned on the cylinder to monitor the position of the piston.
e.g. Reed switch

## Slide 75: Double acting cylinder 3
Types of cylinder mounted sensors available are:
Pneumatic
Electrical
Electronic

## Slide 76: Double acting cylinder 4
With magnetic piston
Allows the position of the piston to be monitored.
Mounting the sensors on the cylinder keeps them out of the work area.

## Slide 77: Electropneumatic symbols

## Slide 78: Switches and contacts

## Slide 79: Switches and contacts 1

## Slide 80: Switches and contacts 2

## Slide 81: Relays, timers and solenoids

## Slide 82: Relays and solenoid coils

## Slide 83: Electrical Symbols

## Slide 84: Electrical Circuits
Identification
System Structure
Basic Logic Functions

## Slide 85: Identification Code for Components
The identification code contains the following information
Unit Number
Circuit Number
Component Identification
Component Number

## Slide 86: Component Number
Within each circuit, components with the same component identification are numbered consecutively from the bottom to the top and from left to right.
For Example:
Directional control valve: 1V1
One-way flow control valve: 1V2

## Slide 87: Electropneumatic Component Identification

## Slide 88: Control System Component Identification

## Slide 89: Control System Component Identification Examples
Manually operated switches S1, S2 and S3.
Limit switches 1S1 AND 1S2.
Pressure switch 1B1.
Relays K1, K2, K3, and K4.
Solenoid coil 1Y1.
Lamp H1.

## Slide 90: System structure
Components in a control system belong to four basic groups:
Energy supply
Input elements
Processing elements
Final control elements & actuators

## Slide 91: Pneumatic component
Actuator
Final Control Element
Energy Supply

## Slide 92: Electrical component

## Slide 93: Electropneumatic elements

## Slide 94: Control chain
SIGNAL FLOW
SIGNAL OUTPUT
SIGNAL PROCESSING
SIGNAL INPUT

## Slide 95: Signal flow

## Slide 96: Basic logic functions

## Slide 97: Basic logic functions 1
Logic operations are funcions which link binaary signals according to the rules of Boolean algebra. Four basic logic operations are available for this purpose.
Identity (YES) Input and output signal have the same status.
Negation (NOT) The output signal has the opposite value to the input signal.
Conjunction (AND) The output signal only has the value 1, if all the input signals have the value 1
Disjunction (OR) The output signal has the value 1, if at least one of the input signals has the value 1.

## Slide 98: Basic logic functions 2
There are four commonly used logic functions in Electro-Pneumatics.
YES Function
NOT Function
OR Function
AND Function

## Slide 99: Basic electrical circuits
YES Function

## Slide 100: Basic electrical circuits 1
NOT Function

## Slide 101: Basic electrical circuits 2
OR Function

## Slide 102: Basic electrical circuits 3
AND Function

## Slide 103: YES Circuit Exercise
Create the YES Circuit on the trainer.

## Slide 104: AND Circuit Exercise
Create the AND Circuit on the trainer.

## Slide 105: Control of a single-acting cylinder
The piston of a single-acting cylinder is to travel out when a push button switch is pressed. When the button is released, the cylinder is to return to the final rear position.

## Slide 106: Direct Method
The circuit is closed when push button switch S1 closes. A magnetic field is produced in coil Y1. The armature in the coil opens the passage for the compressed air. The compressed air flows from 1 to 2 to the cylinder, which travels to the final forward position.
When push button switch S1 is released, the circuit is interrupted. The magnetic field at coil Y1 collapses, the 3/2-way valve switches back to its original position and the cylinder travels to the final rear position.

## Slide 107: Indirect Method
With the indirect method, the push button switch S1 energizes a relay K1. The coil Y1 is energized via a normally open contact of K1 (indirect energizing).
Otherwise the sequence is the same as the direct method.
The indirect method must be applied when the switching capacity of signaling device (S1) is not sufficient to switch coil Y1, or if further processing is required with a different voltage (220V).

## Slide 108: Exercise 1 Realising a Sorting Device
A sorting device is to be used to sort water samples according to the since of the sample bottle.
Pressing of a pushbutton causes the piston rod of a singe-acting cylinder to push the sample bottle off the conveyor.
When the pushbutton is released, the piston rod is to return into the retracted end position.

## Slide 109: Exercise 1
Solution

## Slide 110: Control of a double-acting cylinder
The piston of a double-acting cylinder is to travel out when a push button switch is pressed. It is to return when the push button switch is released

## Slide 111: Exercise 2 Realising a Shut-off Device
In a water treatment system numerous pipes need to be opened or and closed by means of shut-off devices. A test setup is to be used to find a possible means of actuating the shut-off valve.
Pressing of a pushbutton is to cause the valve to open the slide.
Releasing of the pushbutton is to cause the slide to close.

## Slide 112: Exercise 2
Solution

## Slide 113: Exercise 3 Realising a Lid Press
In a filling plant, wall or ceiling paints are filled into plastic pots. Once filled, slip-lids are to be pressed onto the plastic pots.
Pressing of a pushbutton is to cause the pressing ram to advance and the slip-lid to be pressed on.
Once the pushbutton is released, the pressing ram is to be returned into the initial position.

## Slide 114: Relays 2
Allow
  multiple switching operations
  different voltage levels
  different control paths
Used for logic functions and interlocking
Ease of maintenance
Switching cycles ~ 10’s of millions

## Slide 115: Relay
Cover
Return spring
Armature
Coil
Coil connections
A1
A2
Contact connections
Contacts
12
14
Symbol
11
22
24
21

## Slide 116: Relay 1
A1
A2
12
14
Symbol
11
22
24
21
A1 A2 4 2 1

## Slide 117: Relay 2
Symbol
12
14
22
24
A1
A2
11
21
A1 A2 4 2 1

## Slide 118: Relay 3
A1
A2
12
14
Symbol
11
22
24
21
A1 A2 4 2 1

## Slide 119: Relay 4
A1
A2
11
12
14
21
22
24
A1 A2 4 2 1
Symbol

## Slide 120: Relay 5
2 changeover relay
size
14mm x 9mm x5mm

## Slide 121: Relay 6
4 contact relay
Up to 2 x 108
switching cycles

## Slide 122: Exercise 3
Solution

## Slide 123: Parallel circuit (OR logic)
The piston of a double-acting cylinder is to travel out when either one of two push button switches is pressed. It is to return when the both push button switches are released.

## Slide 124: Exercise 4 Realising the Operation of a Hinge Lid
Plastic granulate is to be filled from a storage silo. The silo is to be opened or closed using a hinged lid. The process is to be effected from two points.
Pressing of either one of the pushbuttons is to cause the hinged lid to open and to empty the bulk material form the container.
Once the pushbutton is released, the hinged lid closes.

## Slide 125: Exercise 4
Solution

## Slide 126: Indirect control of a double acting cylinder
The piston of a double-acting cylinder is to travel to the final forward position when push button switch S1 is pressed. It is to remain there until the return stroke is activated via push button switch S2

## Slide 127: Exercise 5 Realising a Diverting Device
Packages are to be pushed from one conveyor to another via a diverting device.
Pressing of a pushbutton is to cause the frame of the diverting device to be advanced. The package is transferred ad transported away.
Pressing of another pushbutton causes the frame to be moved into the initial position.

## Slide 128: Exercise 5
Soluiton

## Slide 129: Automatic return of a double acting cylinder
The piston of a double-acting cylinder is to travel to the final forward position when push button switch S1 is pressed. When it reaches this position, it is to return automatically to its original position.

## Slide 130: Exercise 6 Actuation of a Stacking Magazine
Wooden boards are to be pushed from a stacking magazine into an assembly device.
Pressing of a pushbutton causes a wooden board to be pushed out of the stacking magazine.
Once the forward end position is reached, the slide is moved into the initial position.

## Slide 131: Exercise 6
Solution