## Slide 1: Computer Vision, Motion Control and Communication Design of Autonomous Robots based on Embedded Linux
Chloe Zhu
5/20/26
Chloe.Zhu@Schaeffler.com https://chloezhu1.github.io/

## Slide 2: Agenda
Computer Vision
Motion Control
Communication (Precise Synchronous Frequency Offset Apparatus)
Embedded Linux Application in Robotics

## Slide 3: Embedded Linux in NAO Humanoid
The NAO robotics platform, originally developed by Aldebaran and SoftBank, and now by Maxtronics.
OpenNAO operating system is based on the Gentoo embedded Linux OS, and uses the NAOqi API for autonomous robot control.
We also used the OpenCV computer vision library as part of our open source software stack to program our NAO humanoid robot.

## Slide 4: Robot Golfing Competition
Nao humanoid robot is an autonomous, programmable humanoid robot.
YouTube Link of our robot

## Slide 5: Complete Technical Pipeline
Image Acquisition
Image Preprocessing
Ball Detection — Hough Circle Transform
Ball Recognition Decision
Ball Localization (Distance & Position)
Kalman Filter Tracking
Robot Motion & Golfing
resolution: 640×480 frame rate: 30 FPS monocular vision
RGB, HSV
image pixels → real-world position

## Slide 6: Full Coordinate Transformation Pipeline Ball Detection → World Position
Image Frame
Pixels (u, v)
Optical frame (camera center)
camera frame ray angles pitch, yaw
World frame
intrinsics
head yaw/pitch+mount tilt
Camera pose transform
Image Coordinate System (Pixels)
(center_x, center_y, radius)
image center = (W/2, H/2)
Pixel Offset → Camera Angles
img_pitch = (center_y − img_center_y)/H * cameraPitchRange img_yaw = (img_center_x − center_x)/W * cameraYawRange
Add Head + Camera Mount Angles
camera_pitch = head_pitch + camera_mount_tilt ball_pitch = camera_pitch + img_pitch ball_yaw = head_yaw + img_yaw
Polar → Robot XY Coordinates
disX = distance * cos(ball_yaw) disY = distance * sin(ball_yaw)
Camera Frame → World Frame
ball_world_X = cameraX + disX ball_world_Y = cameraY + disY

## Slide 7
Geometry
X (Forward)
y
Golf ball
camera
Pitch
dpitch
yaw
For quick illustration, I set the x-axis along the pitch distance direction in this example. In general, it’s not true. We need to consider X_camera as well.
dyaw
h-r
Converting camera frame to world frame.

## Slide 8
Compensating y-coordinate in world frame
Physics model
angles → tan → cos → geometry
Empirical model
ky polynomial correction
+
ky = a*ballX**4 - b*ballX**3 + c*ballX**2 - d*ballX + e
ballY = ky * ballY
4th-degree polynomial correction factor applied to Y (lateral distance)
data-driven error compensation
In real robots, geometric model has systematic errors:
camera tilt not exact
head angle offsets
lens distortion
FOV scaling not perfectly linear
camera mount flex
joint encoder bias
ground plane not perfectly flat
image center not perfectly calibrated
1. Collect calibration data: trueX, trueY (measured by tape / motion capture). Run vision system →compute: estX, estY
2. Compute Y error ratio: ky_needed = trueY / estY, as a function of distance: ky_needed = f(estX)
3. Fit polynomial: regression

## Slide 9
Computer Vision: How to select the red ball from the detection?
r
4r
Area_ball/area_square = 0.196
Image Processing flow
Grab the latest camera frame
Set circle detection constraints
Build a “ball-likelihood” grayscale/binary image
Detect circles in that processed image
Select the best circle candidate
Handle “no ball found”
store ball data and compute position
rRatio = rScore / total_pixels gRatio = gScore / total_pixels
Selection Criteria:
if rRatio >= 0.12 and gRatio >= 0.1 and abs(rRatio-0.19) < abs(rRatioMin-0.19):
Condition A — enough red pixels Condition B — enough green pixels
Condition C — red ratio close to target value

## Slide 10
Red ball detection:
Crop the image
Convert BGR → HSV: frameHSV = cv2.cvtColor(frameArray, cv2.COLOR_BGR2HSV)
HSV threshold (binarization): frameBin = cv2.inRange(frameHSV, minHSV, maxHSV)
Erosion: frameBin = cv2.erode(frameBin, kernelErosion, iterations=1)
Dilation: frameBin = cv2.dilate(frameBin, kernelDilation, iterations=1)
Gaussian blur: frameBin = cv2.GaussianBlur(frameBin, (9,9), 0)
Return processed mask
Computer Vision:
remove small noise while preserving shape
Yellow Stick detection:
Capture and crop the image
Find contours in the binary image: _, contours, _ = cv2.findContours(frameBin, cv2.RETR_EXTERNAL, cv2.CHAIN_APPROX_NONE)
Loop through contours and filter by size: Compute perimeter and area, and filter by Size (Only keep contours large enough to be real objects). Get their bounding rectangles.
Shape filter — stick-like aspect ratio: rects = [rect for rect in rects if (1.0*rect[3]/rect[2]) > 0.8]. Recall: rect = [x, y, w, h]
Convert to numpy array

## Slide 11
Choose the “most stick-like” rectangle: Selects the rectangle with largest height/width ratio → most vertical
Adjust Y coordinate back to full-frame space
Continued:

## Slide 12
Closed-loop feedback control using Force-sensitive Resistor (FSR)
Principle: find the robotic I/O layout of analog, GND and 5V (as power). Connect FSR from 5V output, in serial to 10K resistor, then ground. Having analog (ADC) trace the voltage.
Via the circuit and Nao’s Arduino data logger, I could record FSR voltages at regular intervals, thus having pressure information at self-defined sampling rate, to control and adjust the coordinates of the robotic arm hitting the golf ball.

## Slide 13: Correlation between the coordinates and the Force (Voltage/Resistance)
Voltage – pressure
We transfer pressure to a corresponding visible parameter – coordinate. We have x,y,z 3D coordinate in this application. We can break down the coordinates each direction. For simplicity, we take x-direction for demonstration, so we can control x coordinate to control the pressure applied when playing golf.

## Slide 14: Measurement and Data Logging of the Output Voltage
The analog ADC input to Arduino Uno board of Nao for voltage reading. I used the same Arduino Uno board as in the robotic system, and wrote the Matlab script to plot and analyze the relative ADC counts (y-axis) wrt time (x-axis/ms):
a=arduino('/dev/cu.wchusbserial1420','uno');
interval=10000;
passo=0.05;
x=[];
t=1;
while (t<interval)
b=readVoltage(a,'A0');
x=[x,b];
plot(x);
grid
t=t+passo;
drawnow;
end
By setting passo value, I could manage the interval of the sampling.

## Slide 15
Communication Design
What is an effective way to use RF communication without interference with other transmitters?
How do we get precise synchronous frequency signal?
In robotics competition/robotics stage performance, if we use RF communication module, there might be more than 10 robotic teams communicating with robots at the same time, and each team might have multiple robots to control (think of a football team).

## Slide 16
Precise Synchronous Frequency Offset Apparatus in Robotics Application
The Precise Synchronous Frequency Offset Apparatus is an intelligent RF calibration system for robotic communication modules. Using a microcontroller-based architecture and real-time frequency measurement/control, it replaces traditional analog Phase-Locked Loop (PLL) synchronization methods to achieve high-precision synchronous frequency calibration.
processing frequency
transmit
Interlaced scan
Phase-Alternating Line (PAL) – based TV (First scan odd-numbered lines, then even-numbered lines, in total 625H, 312.5H each.)
Extract 20 synchronous pulses to get SF
calibrate Voltage-Controlled Crystal Oscillator (VCXO) against SF
Solution:
Frequency calibration: Standard Frequency (SF) signal 1(MHz) from China Central Television (CCTV).
At 16H and 329H of any CCTV programs, they contain 20 synchronous pulses from cesium atomic clock whose precision can reach 10^{-11} – 10^{-15}.

## Slide 17
Thus, we can assign the frequency to each robot from 200 MHz, step size as 1 MHz increment, e.g. the second robot RF communication can be set as 201 MHz, the third 202MHz, etc.

## Slide 18
Connection to Embedded Linux
Embedded Linux System
NAOqi Middleware
Python Robot Control + Computer Vision
Camera / Motors / Sensors
Autonomous Robot Behavior
Architecture Diagram
Embedded Linux OS
(OpenNAO/NAOqi)
Camera drivers
Actuator motors
NAOqi API
Python/OpenCV App
HSV segmentation
Hough circles
Localization
Motion planning

## Slide 19
NAO Robot Runs an Embedded Linux OS: OpenNAO / NAOqi OS (based on Gentoo)
Vision Pipeline Uses Embedded Linux Camera Interfaces:
Camera Sensor ↓ Linux camera driver ↓ NAOqi camera API ↓ Python/OpenCV ↓ Vision algorithms
Motion Control Uses Embedded Middleware + Hardware Drivers
motionProxy.setAngles(...)
motionProxy.moveTo(...)
These are high-level calls into:
Python API ↓ NAOqi middleware ↓ Embedded motor controllers ↓ Servo actuators
The Linux-based robot OS handles:
actuator communication
scheduling
sensor polling
safety constraints
synchronization

## Slide 20
Real-Time Sensor Fusion on Embedded Hardware
Resource-Constrained Embedded Computing:
HSV thresholding
Used because:
lightweight
efficient
low compute cost
Hough circles
Optimized circle detection:
avoids heavy deep learning models
suitable for embedded CPU
Middleware Architecture
Networking & Inter-Process Communication:
Application Layer Python vision/motion logic -------------------------------- Middleware Layer NAOqi APIs -------------------------------- Linux OS Layer scheduling / networking / drivers -------------------------------- Hardware Layer cameras / IMU / motors / sensors
ALMotion ALVideoDevice ALMemory
NAOqi modules communicate over:
TCP/IP
proxies
shared middleware APIs

## Slide 21: Thank you so much!
YouTube Link of our robot
Chloe.Zhu@Schaeffler.com https://chloezhu1.github.io/